## Slide 1: ATTREX Met Briefing for flight of January 31
Review of weather for flight ops
Temperature conditions in flight region
  Forecast fields
  Hovmöller plot at 10°N [Newman]
Cloud and dehydration conditions in tropopause-level flow - RDF water vapor [Schoeberl]
Rennie Selkirk 30 Jan 2013
Version 2, 10 AM

## Slide 2: 4 AM Thursday – 31 Jan 12UT / GFS 54HR
DISCUSSION
Continued warmer (thickness >552 dam)
Hi pressure [K] still offshore
Weak vort max feature [L]from cut-off low may produce some upper level cloudiness as RH forecast at 500 hPa in this feature is wet (next slide)
Otherwise atmosphere is fairly dry over region[M]
CONTINUED GREAT FLYING WEATHER!!
  .
K
L
M

## Slide 3: 4 AM Friday – 01 Feb 12UT / GFS 78HR
DISCUSSION
Ridge building in [N]; warm (thickness > 552 dam)
Cut off low [O] may induce some high cloudiness
Though atmosphere remains dry at 700 hPa, RH at 500 hPaover region[P]
CONTINUED GREAT FLYING WEATHER!!
N
O
P

## Slide 4: 4 PM Tomorrow – 01 Feb 00UT
Cooling off in target region:
190 K isotherm much closer to W02
Southern leg W03 to W04 now crosses 190 K halfway down
Shift entire pattern east? How much room?
4 AM Today – 30 Jan 12 UT – FH12
100 hPa Temperature evolution

## Slide 5
Eastward extension of cold region
100 hPa Temperature evolution
Time-longitude flight window

## Slide 6
In GEOS-5, skin temp limit (189.5K) reached sooner on approach to W01
GEOS-5 lowest temps – accounting for different isotherms on these plots – are lower in target region
GFS – FH48
Trop/min Temperature – mid-flight – 01 Feb 00UT
GEOS-5 – FH72

## Slide 7
GEOS-5 min T – mid-flight – 01 Feb 00UT

## Slide 8
RDF Results – 01 Feb (Day 2)
Cloud probability
Net dehydration