## Slide 1
The NASA Airborne Tropical TRopopause EXperiment (ATTREX)
Eric J. Jensen 1, Leonhard Pfister1, Troy Thornberry2,3, and the ATTREX Science Team
1NASA Ames Research Center; 2NOAA Earth System Research Laboratory; 3CIRES, University of Colorado
Motivation for the experiment
Processes in the Tropcail Tropopause Layer (TTL) control the input of trace gases into the stratosphere. The most important of these is water vapor, which is important both for the ozone budget and for climate. The overarching objectives of ATTREX are to improve our understanding of how deep convection, slow ascent, waves, and cloud microphysics control the humidity and chemical composition of air entering the stratosphere.
A critical process in maintaining water vapor in the stratosphere is the formation of thin cirrus sheets near the cold tropical tropopause. The freeze drying process is complicated by convection, horizontal variations in temperature and vertical ascent rates, and the fact that ice crystal nucleation processes at cold temperatures are poorly understood. ATTREX is a five year airborne science experiment focused on understanding TTL processes. This poster reports on some results from the first three ATTREX flight series that took place in October-November, 2011, February-March, 2013, and February–March, 2014.
Aircraft and instrumentation
Global Hawk Unmanned Air System
15 – 20 km ceiling
25-hour (10,500 nmi) duration
~1,000 lbs payload
Temp profiler
Whole air sampler
P, T, winds
Radiometers
Chromatograph
Cloud Lidar
IR spectrometer
DLH Water vapor
Mini-DOAS
NOAA Water
FCDP Cloud probe
Ozone
Pressurized compartments
Unpressurized compartments
Oct–Nov 2011, Jan-Feb 2013, and Feb-Mar 2014 Flights
Flight durations ranged from 12 to 26 hours
Cold tropopause regions, convective detrainment, and tracer gradients targeted
Sampling in eastern, central, and western Pacific
Numerous vertical profiles through the TTL (14–19 km)
Combination of CPL lidar and in situ measurements provides unprecedented information about TTL cirrus structure and microphysical properties. (Courtesy A. Rollins)
Measurements of TTL, water vapor, clouds, and tracers
Coordinated campaigns in Guam provided halogen measurements from the surface to the lower stratosphere [E. Atlas, M. Navaro, CONTRAST and CAST investigators]
Data access
ATTREX TTL sampling statistics:
>200 hrs of TTL sampling
~300 TTL vertical profiles
CAM-Chem: Variability and Distribution of Organic Bromine Species
WESTERN PACIFIC
EASTERN PACIFIC
Halon 2402
Halon 1211
CH3Br
Minor VSLBr
CHBr3
CH2Br2
Alt (Km)
Mixing ratios (pmol/mol)
Bin 1Km Alt
Error model and measurements =1sd
Spheroids
Columns
Budding
Rosettes
Rosettes
NASA Global Hawk
UK BAe146
NCAR GV
Sampling near Typhoon Faxai east of Guam
Hawkey CPI images of TTL ice crystals [P. Lawson, S. Brooks]
Hawkey FCDP and 2DS provide full ice crystal size distributions from 1–2000 μm. [P. Lawson, S. Brooks]
Excellent agreement between DLH [G. Diskin], NOAA H2O [T. Thornberry, A. Rollins], and frostpoint balloon [D. Hurst].
Ice crystal number concentrations consistent with measured ice supersaturation [Jensen et al., 2013, PNAS]
Evaluation of global-model cloud parameterizations using Hawkeye data [C. Bardeen]
Evaluation of global-model halogen simulations using GWAS measurements [M. Navaro, A. Saiz-Lopez, and X. Rodriguez-Lloveras]
Hawkeye
Data archive:
espoarchive.nasa.gov/archive/browse/attrex
2011 and 2013 data publicly available
2014 data will be public in early 2015 (contact ATTREX investigators for access now)
AGU ATTREX presentations